Problems [Ch. 4]

1. Derive that, in the two-phase region,

1) G = [ρf - ΔρCo<α>]<j> - ΔρVgj<α> , where Δρ = ρg - ρf

2) j = ufo[1+x(vg/vf-1)] , where ufo is the inlet velocity to an evaporating

Tube

2. Derive the cross-section averaged void propagation equation from the vapor continuity equation. Describe the exact definitions for Co and Vgj.

3. Solve the following Problem (2-1) in Collier's book.

4. In a vertical tube(D=1cm, L=2.5) heated uniformly at 100kw, the saturated water flows in with G=0.12kg/s under p = 70 bar. Derive the frictional pressure drop through the tube with a homogeneous and separate flow model.

5. Derive the nodal one-dimensional two-phase conservation equations for mass, energy and momentum.

Assume the upper boundary of the node is fixed, but the lower one is moving [e.g. the boiling boundary, Lo(t)].

Note : Relate the node-average parameters to

the arithmetic average of the corresponding node inlet and outlet parameters.

6. Plot the void fraction versus quality for the bulk boiling of water in a 1" I.D. tube at 1000 psia and G = 1 x 106 lbm/hr-ft2, using the Zuber-Findley model (use Co = 1.1, k3 = 1.53).

7. For a rectangular subchannel of 14ft long, plot the total static pressure drop along the heated length as a function of mass flux(i.e. ,plot Δp vs G). (neglect subcooled boiling region) Show the various pressure drop component.

coolant pressure 1000 psia

pitch to diameter of fuel rod 0.5 / 0.7 in

power density(q') 7.0 KW/ft

inlet coolant temperaqture 520 oF

8. For the case of ideal annular flow (i.e. annular flow with no liquid entrainment, no void in liquid film and smooth surface interface) in a pipe. Derive values fro the drift-flux parameters, Co and Vgj. How do these parameters change for the cases of counter-current flow?

9. Show that an j can be expressed in term of the inlet velocity to an evaporating tube, ufo, the mass quality, x, and the phase specific volumes, vg and vf, as follows;

10. Consider a rectangular subchannel having the pitch of 0.7 in. in a reactor of pressure of 1000 psia. The length and outer diameter of fuel rod is 14 ft and 0.5 in, respectively. The rod produces axialiy uniform heat of 17kw/ft. When the coolant flows at the inlet with 520 F and 6ft/sec, calculate the axial steady-state void fraction profile with following models.

1) the profile fit model

2) the mechanistic model with HEM

3) the mechanistic model with

11. In Problem10, calculate the pressure drop in the subchannel when the inlet coolant flow varies from 1 to 20 ft/sec.

Use  ① HEM

②