## Slide 1: Dye-sensitized Solar cell
2002-11971 박준모
2002-12009 배세영

## Slide 2: How did we get this topic?
Is there any reverse process?

## Slide 3: Necessity of SOLAR CELL
Limit of Natural Source
Increasing the price of oil
Solution for problems the we face

## Slide 4: History of SOLAR CELL

## Slide 5: The Spectrum of Solar Energy

## Slide 6: From now on, we are going to focus on DYE-SENSITIZED SOLAR CELL

## Slide 7: Why DSC?
Very low cost fabrication
Attractive features that
facilitate market entry
Good for everyone

## Slide 8: DSC Structure(overall)
Oxide
Semiconductor
Dye Sensitizer
Electrolyte

## Slide 9: DSC Operation
-S+/S → S+/S*
-Electron injection to
conduction band of TiO2
-e- to counter electrode
via external load
-I3- + 2e- → 2I-
-2I- → I3- + 2e- (to dye)

## Slide 10: Material for DSC(Oxide Semiconductor)
Wide Band gap
Nanoporous structure
Low cost, non-toxic, biocompatible
Low porosity
M.Gratzel, Dye-sensitized solar cells,2003

## Slide 11: Material for DSC(Dye Sensitizer)
-Concrete bonding to TiO2
-Absorption of whole region of visible rays
-Should be stable optically and thermally

## Slide 12: Material for DSC(Electrolyte)
Reduction & Oxidation
Provide electron to DYE
Platinum( Catalyst ) – related to the speed of electron while luminescence

## Slide 13: Current Issue( Nanowire DSC)
Advantage
  -Rapid collection of
  carriers
  -Uniform electrolyte
  contact
Disadvantage
  -Surface area up to 1/5
  -Low efficiency(1.5% at
  full Sun)

## Slide 14: Current Issue(Quantum dot)
Zero-dimension structure
The absorption can be
adjusted by changing the
particle size
High extinction coefficient

## Slide 15: Current Issue(solid-state DSC)
-Liquid electrolyte →
transparent p-type
Semiconductor
-n-type TiO2 Dye p-type CuI
-Carrier Separation
D + hv → D*
D* → D+ + e- (to CB of TiO2)
D+ → D + h+ (to VB of CuI)
-Low efficiency (4.6% at full
Sun)

## Slide 16: Advantage of DSC
Insensitive to angle of incident
Low cost
Durability, Flexiblity
Able to produce transparently
→ Able to produce multi-layer cells
→ Improve the efficiency in same area

## Slide 17: The present DSC technology in KOREA
KIST, ETRI, KERI
Able to mass produce 1st and 2nd generation SOLAR CELL
Lack of an infrastructure to produce 3rd generation SOLAR CELL

## Slide 18: THE END Thank you for your patience