## Slide 1
November 11. 2014
Gasification Technology of Solid wastes
KWAK YEON HO
KOLON GLOBAL Corp., R&D department
Seoul National University Seminar

## Slide 2
1. Introduction of KOLONGLOBAL
[Gwacheon]
▶ KOLON GLOBAL CORPORATION
▶ Address
- KOLON TOWER (Main building) 11 kolon-ro
Gwacheon-si, Gyeonggi-do, Korea
▶ Revenue : 3 Billion Dollars (2013)
[Songdo]
- Song-Do Technopark IT Center 32 Song-Do science-ro
YeonSu-Gu, Incheon, Korea
KOLON GROUP
Established in 1954
Over 12,000 employees with 36 Subsidiaries
Sales Revenue US$ 11 Billion (2013)
▶ Employee : 2,500 people
[Overview]

## Slide 3
1. Introduction of KOLONGLOBAL
1954
Kaemyeong Corporation formed
Trading
1990
KOLON Communication and Information
IT
2006
KOLON I’Net
2001
KOLON
International
1987
(Established)
KOLON Motors
1984
(Established)
KOLON SPOREX
Sports & HealthCare
Motors
1960
(Established)
Hyupwha Industry
Construction
1978
KOLON General Construction
2000
KOLON E&C
Engineering
[Merger]
1977(Established) KOLON Engineering
2005
KOLON
Glotech
2011
(Spin-off)
KOLON B&S






[History of Company]
Merger-Launched in Dec.2011
[Name Changed]
[Name Changed]
1979
KOLON
Trading Corporation
[Merger]
[Name Changed]
[Merger]

## Slide 4
1. Introduction of KOLONGLOBAL
Construction
- Construction, Development, EPC & O&M
- Power plant, Environmental plant
- New regeneration energy
- Overseas
Trading Service
- Steel
- Energy, Heavy chemistry
- Fashion, Leisure, Fiber
- General products
Health care
- Sport center (KOLON Sporex)
- Lifestyle Business (Bang&Olufsen)
Auto distribution
- BMW Dealing (No.1 in domestic)
A/S Factory
BMW Rental, Lease
BPS service
MINI, R/R, BMW Motorrad
Portfolio
[Business Area]

## Slide 5
1. Introduction of KOLONGLOBAL
Green technology for the future
Future Environmental Technology for Human
Base on environment friendly technologies and abilities, KGC provides total solution for all environmental facilities from EPC to O&M.
Our sewage water treatment technology is selected as new
environmental technology and we’re endeavoring to improve
high water treatment facilities business.
Water treatment
Waste treatment(Incineration, Sanitary landfill)
Waste to Energy
Recovery works, etc.
Business Brief
Namyang-Ju Incinerators
Daejeon Sewage Treatment Plant
Chiang Mai in Thailand
Water Supply Facility
Deoksan Water Purification Plant
[Environment Business Area]

## Slide 6
2. What is Gasification?
Thermal treatment technology of wastes

## Slide 7
2. What is Gasification?
Combustion
Gasification
Pyrolysis
Excess Air
Partial Air
No Air
Heat
Ash
Syn gas
Ash
Liquid
Gas, Char
공급원료
C
H
N
S
O
CO2
H2O
NOx
SOx
O2
CO, CH4
H2, H2O
NOx
SOx
O2
Gasification
Partial combustion reaction
Combustion
Complete combustion reaction
Thermal Process
Thermal Conversion Processes : Combustion, Gasification, Pyrolysis

## Slide 8
2. What is Gasification?
Air-fuel ratio, %
Pyrolysis zone
Gasification zone
Combustion zone
Thermal Conversion Processes : Combustion, Gasification, Pyrolysis

## Slide 9
2. What is Gasification?
The feedstock is prepared and fed into a gasifier with the reactants
Combustible gas called syngas is produced
These gases are available to produce the electricity or heat after gas cleaning
They can also be used for the production of chemicals
Coal (Char)
Waste
Biomass
Residual Oil
Gasifier
Temp. : 700~1,500℃
Syngas
Boiler
Turbine
Engine
Fuel Cell
Synthesis
Electricity
Heat
Methanol
DME
F-T
Ammonia
Hydrogen
SNG
Air, O2, Steam
Inorganic matters
CO, H2, CH4
Energy = Heat
+ Chemicals
Purpose : To convert wastes or low-value fuels to higher value energies

## Slide 10
2. What is Gasification?
8/21
Ash / Slag / PM / Tar
Combustion reactions,
C + 1/2O2 ↔ CO
C + O2 ↔ CO2
H2 + 1/2O2 ↔ H2O
Boudouard reaction,
C + CO2 ↔ 2CO
Water gas reaction,
C + H2O ↔ CO + H2
Methanation reaction,
C + 2H2 ↔ CH4
CO shift reaction,
CO + H2O ↔ CO2 + H2
Steam methane reforming reaction
CH4 + H2O ↔ CO + 3H2
Syngas
Composition (Vol %)
H2
CO
CO2
CH4
H2O
H2S
N2
NH3+HCN
25 - 30
30 - 60
5 - 15
0 - 5
2 - 20
0.2 - 1
0.2 - 1
0 - 0.3
Waste
Oxygen
Steam
Main gasification reaction and gas composition

## Slide 11
3. Why is Gasification?
Advantages of Gasification in compare to incineration
Environmental standpoint
  low SOx / NOx emissions(reducing atmosphere)
  Dioxin compounds are not formed during gasification
  Reduction of CO2 emissions
  (Exhaust gas is much less than its of combustion)
Energy standpoint
  Possible to a various applications(Power/Heat/Chemicals/Oil)
  Power efficiency is high
By-product utilization standpoint
  Reuse of slag as construction materials

## Slide 12
3. Why is Gasification?
Classification | Reduction of greenhouse gas (TC/ton) | Reduction of others (TC/ton) | Total (TC/ton)
Incineration (No heat recovery) | 0 | - | 0
Incineration (With Heat recovery) | 0.19 | - | 0.19
SRF (Solid refused fuel) | 0.21 | - | 0.21
Gasification | 0.27 | 0.4 | 0.67
Reduction effect of greenhouse gas according to waste to energy types

## Slide 13
4. What do we develop?
type | Fixed bed | Fluid bed | Rotary kiln
Advantage | Simple of gasifier | High heat transfer Large scale upgrading | High syngas quality (indirect heating)
Disadvantage | Limited capacity | Low syngas quality (high air injection) | Low heat transfer
Development of gasifier

## Slide 14
4. What do you develop?
Contaminant | Examples | Problems | Cleanup method
Particles | Ash, char, fluid bed material | Erosion | Filtration, scrubbing
Alkali Metals | Sodium and potassium compounds | Hot corrosion | Cooling, condensation, filtration, adsorption
Fuel nitrogen | Mainly NH3 and HCN | NOx formation | Scrubbing, SCR
Tars | Refractory aromatics | Clog filters, difficult to burn, deposit internally | Tar cracking, Tar removal
Sulfur, Chlorine | H2S, HCl | Corrosion, emissions | Lime or dolomite scrubbing or absorption
Development of gas cleanup system

## Slide 15
4. What do you develop?
Structure of tar
Development of gas cleanup system
As complex aromatic compounds are connected with many benzene rings, tar is very difficult
to remove completely.
The tar is present in the gaseous state at a high temperature.
However, tar is changed in a limy liquid when cooled.
This can cause the damage to the engine or turbine equipment

## Slide 16
4. What do you develop?
Physical removal method
To directly remove the tar
Filter
Scrubber
Adsorption
Low cost
Low removal efficiency
Reduction of syngas heating value
Steam reforming method
Tar was converted into syngas by a thermochemical conversion
Steam of a high temperature
High value syngas
High removal efficiency
High cost
Tar removal method
Development of gas cleanup system

## Slide 17
4. What do you develop?
LPG
Tank
Generator
Power Meter
Air
N2
CO2
CO
H2
MFC
MFC
MFC
MFC
MFC
Engine
MFC manager
DAQ system
MFC
Emcoder
Taco meter
Sensor
LPG (5.4LPM)
Test of gas engine
RPM : 3200 rev/min
LPG (5.4LPM)
RPM : 1800 rev/min
LPG (3.3LPM)+CO2(2.1LPM)
the gas engine for LNG was generally developed
Heating value of syngas is very lower than its of LNG (1,500kcal/Nm3)
When heating value of syngas is low, techniques for controlling the mechanical characteristics of engine is needed.
Development of gas engine

## Slide 18
5. Our research
Project Title | Eco-STAR Project : Center for Waste Eco-Energy and non-CO2 Green House Grasses
Research Title | Development of energy conversion technology from waste through application of pre-treatment & gasification
Total Research Period | 2008. 2.1~2012. 12.31 (4 year 10 month)
Total Research fund | 8.2 billion won
Major Research Institute | KOLON E&C
Participating firm | KOLON E&C, EFMC, KOREA DISTRICT HEATING CORP, SUDOKWON Landfill Site Management Corp., SEOHUNG EN-TECH LTD., U SENTECH
Consignment research institution | Korea Testing Laboratory, THE UNIVERSITY OF SEOUL
Research Project

## Slide 19
5. Our research
Objectives
Concept : E3 TECHNOLOGY
Eco – friendly : Developing technologies to minimize contaminants
Energy efficient : Maximizing recovery of energy by increasing gasification conversion rate
Economic : Saving cost of facilities and operation by integration and localization
Developing energy conversion system from waste by pretreatment / gasification / energy recovery technologies
Application in full-scale plant

## Slide 20
5. Our research
2008
2009
2010
2012
Research project launched(2008)
Manufacture of gasification
facility(2011. 05)
Operating and test(~2012)
Prototype manufacture and test(20kg/hr) (2009)
Plant design(5t/d)(2010)
Manufacture of pre-treatment facility(2010)
Construction of building
(2010)
2011
Research history

## Slide 21
5. Our research
Prototype rotary kiln gasifier(20kg/hr)

## Slide 22
5. Our research
Feeding rate : 15-17kg/hr
TC1 temperature : 630 – 790 C
Air ratio : 0.05 – 0.15
Cold trap
RDF
TC1
TC2
TC3
Micro GC
LPG Burner
Inlet
Outlet
Char box
Gas sampling
Syn gas
Flare stack
Exhaust gas
Stack
Testing procedure in a rotary kiln gasifier

## Slide 23
5. Our research
Proximate analysis (wt%) |  | Ultimate analysis (wt%) | 
Moisture | 9.0 | C | 40.63
Volatile matter | 53.0 | H | 5.74
Fixed carbon | 11.5 | O | 23.97
Ash | 25.8 | N | 1.33
High Heating value | 3,850 | S | 0.01
(kcal/kg) |  | * Dry basis, **Wet basis | 
Sample used in this Test
Pelletized RDF

## Slide 24
5. Our research
Feedstock
: RDF(dried and crushed)
Sample weight
: 10 mg
Setting temperature
: 30C/min to 900°C
Carrier gas : N2
2nd stage pyrolysis
1st(300-410°C) : Paper, Wood, Food waste, Textile
2nd(420-510°C) : Rubber, Plastics
TG and DTG curves of Sample

## Slide 25
5. Our research
Hydrocarbons were converted into CO or CO2 by oxidation reaction as AR increased
Result of gasification experiment - gas composition
Air ratio=0.15
Air ratio=0.05

## Slide 26
5. Our research
Heating value(kcal/Nm3)
=Σ(Heating value of each gas * content)
Cold gas efficiency(%)
Heating value in product gas[kcal/hr]
Heating value in RDF[kcal/hr]
Minimum heating value for the energy
from gas engine
: 1300-1,500kcal/Nm3
Cold gas efficiency at high temperature
: 60-70%
An efficient energy generation appears to be possible through results obtained in this experiment
Result of gasification experiment
– Heating value & Cold gas efficiency

## Slide 27
5. Our research
K-MeGa system(Kolon Mechanical & Gasification system)
Waste : Municipal Solid Wastes
Facilities : Pre-treatment + gasification
Capacity : 5 ton/day
Construction costs : 2.1 billion won
Pilot plant
Pre-treatment system
Gasification system

## Slide 28
6. Our research
The video to explain
K-MeGa system

## Slide 29
5. Our research
Research result
Certification on environment new technology

## Slide 30
5. Our research
Research result
Certification on environment new technology

## Slide 31
5. Our research
Research result
Patent application : 36, Patent registration : 12

## Slide 32
6. Our further research _ commercial plant development PJT
Research period : 2013 ~2019(during 9 years)
Research fund : 68 billion won
PJT Scale : SRF 120ton/day, gasification & power 80ton/day
Gasifier type : Fixed bed
Site : Yeosu city
Research institute : Samho, Kolon, Advanced tech. Institute
The first full scale commercial plant in Korea
The next-generation technology alternating incineration
Overview
Meaning

## Slide 33
Thank you for your attention