## Slide 1: Environmental Thermal Engineering
Lecture # 17
Min soo Kim
Mechanical & Aerospace Engineering

## Slide 2
Natural energy sources Solar Energy

## Slide 3: Solar Generation
Very low running cost
No mechanical vibration, no noise
Life of solar cell is more than 20 yrs
Infinite energy source
No pollutant generation
Advantages

## Slide 4: Solar Generation
Solar cell is very expensive
High initial cost
Variation of energy generation since cloudy or rainy weather
Need large area
Low energy density
Disadvantages

## Slide 5: Solar Generation
Classification
Photovoltaic system
 Photo + Volta
Generation with light, useful for an isolate home generation
Solar heat system
 Use solar heat
Generation with heat, useful for power plant

## Slide 6: Photovoltaic generation
Energy generation with the light
Photovoltaic effect is used
Relatively low power(~1.5W)
 Module is used
Energy generation efficiency is about 10~15%
For cloudy day and night, storage battery is used
N-type
P-type
+
+
+
+
+
+
+
-
-
-
-
-
-
-
Wire
Wire
N-type
P-type
+
+
+
+
+
+
+
-
-
-
-
-
-
-
When cell is exposed
Wire
When cell is not exposed
Wire

## Slide 7: Photovoltaic generation
Photovoltaic cells
The photovoltaic cells were developed at Bell Labs in 1950 primarily initially for space applications.
The Hubbell telescope utilizes solar panels for its energy requirements.
Very expensive
: Silicon purification is difficult and a lot of silicon is wasted
Cooling system needed
: high temperature lowers system efficiency

## Slide 8: Photovoltaic generation
Monocrystalline Silicon Cells
: High efficiency (~15%)
Complicate manufacturing process
Multicrystalline Silicon Cells
: Slightly less efficiency (~12%)
Simple manufacturing process
(a) Monocrystalline type
(b) Multicrystalline type
Type of photovoltaic cell [1]

## Slide 9: Photovoltaic generation
Amorphous Silicon
: Absorbs light more effectively
 Thinner film
Can deposit both rigid and flexible bodies
Less efficiency (~6%)
Type of photovoltaic cell [2]
(c) Amorphous type

## Slide 10: Photovoltaic generation
Solar cell
Secondary
Generator
Power
Control
system
Charger
Inverter
Storage
Charger
Electricity
Energy is stored in a storage charger in a daytime
For long time cloudy weather or emergency case, Secondary generator is required
Inverter converts DC to AC
(Solar cell generates DC)
Energy generation Chart

## Slide 11: Photovoltaic generation
Stand-alone system
Hawa-island(60KW)
Wa-island(30KW)
Grid-connection system
Changwon City Hall(30KW)
Samsung Laboratory(100KW)
Solar light
Generator
System
Power Plant
Solar light
Generator
System
Grid connection system
Stand alone system
Classification of photovoltaic generation

## Slide 12: Photovoltaic generation
Energy is stored in a storage charger for night
Cost of a storage charger is very expensive
 Use power control system
For long time cloudy weather or emergency case, Secondary generator is required
A street lamp with photovoltaic generator
Properties

## Slide 13: Photovoltaic generation
Cost?
From www.southwestpv.com

## Slide 14: Photovoltaic generation examples
Photovoltaic generator in Germany
(Rotating toward the sun)
Photovoltaic generator in Germany
(Schlierberg, Germany)

## Slide 15: Photovoltaic generation examples
Photovoltaic generation ferry
(Sydney)
Photovoltaic generator in satellite

## Slide 16: Photovoltaic generation examples
Future : Photovoltaic generation in the moon
Solar energy in the moon is approximately
Energy is transferred to earth by microwave
24 hours full time generation
(independent of weather)
Module size is 10x5[km] and receiving antenna diameter is 10~13km to produce 10GW

## Slide 17: Solar heat generation
G
Heat exchanger
Solar heat Concentrator
Pump
Turbine
Generator
Concentrate solar heat to over 400℃ with reflector
Turbine produce electricity with high temperature steam water
Dessert is suitable for solar heat generation since strong solar radiation quantity
Energy generation with solar heat

## Slide 18: Solar heat generation
Trough type
California, USA(354MW)
Rotate toward the sun
Classification of solar heat generation [Trough]
Schematic of Trough type
Trough type generator

## Slide 19: Solar heat generation
Dish/engine type
Receiver get heat energy by
Concentrator
Classification of solar heat generation [Dish/engine]

## Slide 20: Solar heat generation
Classification of solar heat generation
Component of dish engine type generator
Schematic view of receiver
Receiver
Concentrator

## Slide 21: Solar heat generation
Power tower type
Classification of solar heat generation [Power type]
Schematic of power tower type
Power tower type generator

## Slide 22: Solar heat generation examples
Power tower type solar power generator in Canada
Power tower type generator

## Slide 23
Natural energy sources Ocean Thermal Energy Conversion (OTEC)

## Slide 24: Ocean Thermal Energy Conversion
Definition : Ocean Thermal Energy Conversion
Seawater temperature is almost constant
More than 15℃ difference in Tropical region
 Power generation is available by using temperature difference in the sea
20℃ - Hot
5℃ - Cold

## Slide 25: Ocean Thermal Energy Conversion
Heat exchanger
Pump
Turbine
Generator
G
Heat exchanger
Deep cold water in
Shallow warm water in
Theory
Heating with shallow warm seawater
 Evaporator
Cooling with Deep cold seawater
 Condenser
For vaporization, Closed cycle and refrigerant is used

## Slide 26: Advantages of OTEC
Infinite energy source
No pollutant generation
24 time full time generation ability
Adjustable generation quantity
Produces desalinated water for industrial, agricultural, and residential uses
Very low running cost

## Slide 27: Disadvantages of OTEC
Consideration erosion by seawater
Need optimized refrigerant
Need large thermal difference
(tropical region is suitable)
Low system efficiency
A 100 MW OTEC plant would need to pump 450 cubic meters of both cold & warm water and would require a cold pipe of 20 metres diameter

## Slide 28: Ocean Thermal Energy Conversion
Suitable area for OTEC
Temperature difference is over 20 Celsius degree
Near term and continental shelf is preferred
(Safety and maintenance cost)
Narrow shelves
Temperature difference in the world

## Slide 29: Ocean Thermal Energy Conversion
Classification of OTEC : Closed cycle system
Use refrigerant to generate electricity
Simple and efficient cycle
Efficiency of energy conversion
 5%
Efficiency of entire system
 2.5%
Low construction cost
Closed loop system

## Slide 30: Ocean Thermal Energy Conversion
Classification of OTEC : Open cycle system
Use warm seawater as working fluid
Warm surface water is evaporated under a partial vacuum
Efficiency of energy conversion
 5.5%
Efficiency of entire system
 3%
Generate fresh water
Open loop system

## Slide 31: Ocean Thermal Energy Conversion
Hybrid OTEC system
Classification of OTEC : Hybrid OTEC system
Combine open and closed cycle system
Efficiency is high but initial cost is high
Generate fresh water

## Slide 32: OTEC examples
1KW OTEC system
Open Cycle OTEC in operation at Keahole Point, Hawaii Island

## Slide 33
Natural energy sources Geothermal Energy

## Slide 34: Geothermal Energy
Definition 1 : Use hot water to generate energy
Use HOT water from earth as energy source for electricity or heating
Temperature 20~150℃
 Supply heat energy to demands
Temperature 102-182℃
 Can generate electricity
Very simple and low running cost

## Slide 35: Geothermal Energy
Properties
Very high efficiency  Approximately 50~70%
Needs separator to remove water
Generate a small amount of HSO4
Very limited energy source site
Limited resource quantity
Extract rate is much more than recovery rate
Difficulty to transfer heat energy far
Unrecoverable energy

## Slide 36: Geothermal Energy
Geothermal energy generation : Property
Unlimited resource quantity
No pollutant generated
High energy efficiency
Difficulty to transfer heat energy far
Very limited energy source site
Geothermal power plant

## Slide 37: Geothermal Energy
Classification of Geothermal Generator [1]
Hot steam type
Used if energy source is primary steam
Very early method
Dry steam power plant

## Slide 38: Geothermal Energy
Flash stream type
Used if energy source is primary water
Fluid is sprayed into a tank held at a much lower pressure than the fluid
Flash stream power plant
Classification of Geothermal Generator [2]

## Slide 39: Geothermal Energy
Binary cycle power plant
Most geothermal areas contain moderate-temperature water
 Difficulty in vaporization
Refrigerant is used
No gases is emitted
Classification of Geothermal Generator [3]
Binary cycle power plant

## Slide 40: Geothermal Energy
Extract rate is faster than recover rate
Limited energy amount
Limited suitable area
Problems
Is there more efficient geothermal system?

## Slide 41: Geothermal Energy
Use the earth infinite Heat source and sink
Heat pump system using the earth as heat source and sink is suggested
Temperature of the earth is almost constant independent of weather, climate
Work as heat sink in the summer
Work as heat source in the winter
Ground

## Slide 42: Geothermal Energy
Heat pump using geothermal method
Ground
Evaporator
Condenser
Outdoor unit
Expansion valve
Compressor
Heating mode in winter
Indoor unit

## Slide 43: Geothermal Energy
Geothermal Heat pumps
Ground source heat pump
Geothermal earth connection subsystem
Geothermal heat pump subsystem
Geothermal heat distribution subsystem
Enables heat pump system in Korea

## Slide 44: Geothermal Energy examples
Geothermal power plant
(New Zealand)
경기도 수원 농업기술연구원
비닐하우스 - 냉/난방 운용(50평×2동)

## Slide 45
Natural energy sources Wind Force Energy

## Slide 46: Advantage of Wind force generation
Very low running cost
Infinite energy source
Almost no pollutant generation
Can be constructed in a small area
Good energy source for island
A ground can be utilized with other industry at the same time

## Slide 47: Disadvantage of Wind force generation
Restricted area only
(wind velocity must be over 4 m/s)
Energy generation fluctuation as wind velocity
Limitation of blade size
Noise problem

## Slide 48: Wind force generation
Wind force generation in the world (2000)
Country | Capacity (MW)
USA Denmark Germany Holland Spain Sweden U.K China India Korea | 2141 1420 2874 379 880 176 338 200 992 3

## Slide 49: Wind force generation
Active yaw control (rotation)
Wind blade braking system
pitch control
drum breaking
Higher efficiency for large size
Lower noise for large size
More dead zone for large size
Lighter blade weight
Wind Turbine
Schematic of Wind turbine

## Slide 50: Wind force generation
Component of wind turbine : Blade
Changing the Wind Speed Changes Wind Direction Relative to the Rotor Blade
Blades twists
Made of glass fiber reinforced plastics for weight and strength
Natural frequency test
Wind blade rotation

## Slide 51: Wind force generation
Gray vertical bar
: Obstacle (20m tall)
Yellow vertical bar
: Turbine tower(50m tall)
Blue number
: Ratio of velocity with obstacle
To get 90% wind velocity ratio, tower must be away from obstacle at least for 300m in this case
Wind Shade [1]
Wind Shade for wind velocity

## Slide 52: Wind force generation
Wind energy is in proportion to the cubic of wind velocity
To get 70% wind energy ratio, Turbine tower must be away from obstacle for at least 321m in this case
Avoid obstacle around wind tower
Wind Shade [2]
Wind Shade for wind energy

## Slide 53: Wind force generation
Wake effect and park effect
Tower distribution for park effect
(Approx. 5% energy loss)
Wake effect from wind turbine

## Slide 54: Wind force generation
Speed up effect : Tunnel effect and Hill effect
Tunnel effect
Hill effect

## Slide 55: Wind force generation
Good wind velocity and consistency
Tunnel Effect
No strong blast, no turbulent flow
No obstacle around the generator
No excessive snow, no severe cold
(high altitude area suggested)
Not often lightening area
Suitable area for wind force generation

## Slide 56: Wind force generation examples [1]
Wind turbine in the seaside
(Vindeby, Denmark)
Wind turbines
(Blyth, U.K, 90MW, Biggest)

## Slide 57: Wind force generation examples [2]
Wind turbines in the sea
(Denmark)
Wind turbine
(Daebo, Korea)

## Slide 58
Natural energy sources Wave force generation

## Slide 59: Advantages of wave force generation
Small area for small energy
 light house
24-hour generation
High wave altitude is needed
 2m high wave has 2 kW per seashore 1m

## Slide 60: Disadvantages of wave force generation
Not constant wave velocity
(backward wave, no wave)
High initial construction cost
Difficulty in building facilities in the sea
Hard condition such as erosion
Low energy density
No wind!

## Slide 61: Wave force generation
High wave
: 2m high wave has 2kW per
seashore 1m
Suitable small area needs small energy such as light house
Suitable area wave force generation
Wave energy levels (kW/m of wave front)

## Slide 62: Wave force generation
Kinds of wave force generator : Floating or Pitching Device
Salter Duck wave energy conversion system
Floats or Pitching Devices method
Efficiency is high
Amount of generation is small

## Slide 63: Wave force generation
Air
Generator
Wave
Shore
Schematic of on shore wave force generation
Kinds of wave force generation : Oscillating water column method
Schematic of off shore wave force generation
Sea level rise
Sea level fall
Air
Wave
Air
Generator
Turbine

## Slide 64: Wave force generation
 | On shore | Off shore
Type Survivability Number of Sites Intensity of wave energy Fabrication Environmental | Modular Good Unlimited Very high Simple & inexpensive Non visible/non audible Protects coastline | Monolithic A potential problem Very limited Greatly reduced Complicated & expensive Visible/audible Damages coastline
Comparison of Oscillating water column methods

## Slide 65: Wave force generation
Kinds of wave force generation : Wave Surge or Focusing Devices
TAPCHAN wave energy device
Transferring or focusing the wave to concentrate energy
Water stored in reservoir generates electricity

## Slide 66: Wave force generation examples
Wave force generator
(Floating or pitch type)
Buoy with wave force generator

## Slide 67: Wave force generation examples
Wave force generating ferry - Mighty whale
Developed in Japan(1998)
Use wave force as main energy source
High construction cost
Not available when wave is calm
Prototype : Kaimai(1978)
Mighty Whale

## Slide 68: Wave force generation examples
Wave force generating ferry - Mighty whale and Kaimai
Mighty Whale (cross sectional view)
Wave force generation ferry
Kaimai (made in 1978)

## Slide 69
Natural energy sources Tidal power generation

## Slide 70: Tidal power generation
Theory
Store seawater in flow and rotate turbine with stored seawater in ebb
Generation can carry out twice in flow and ebb
The water level difference must be over 1m
There’s time cannot generate electricity twice in a day
Tidal power plant

## Slide 71: Tidal power generation
Very low running cost
Infinite energy source
No pollutant generation
Advantages of tidal force generation

## Slide 72: Tidal power generation
High construction cost
Very restricted area only
Difference of sea water level in flow and ebb isn’t constant
Must consider environmental problem
Need large area for reservoir
There’s time cannot generate electricity
Disadvantages of tidal force generation

## Slide 73: Tidal power generation
Situation of tidal power in the world
Power plant
Rance (France, 240 MW, biggest)
Annapolis(Canada, 20 MW)
Kislaya(Russia, 800 KW)
Changsia(China, 3 MW)
Potential area in Korea
Garolim(40 MW)
Sihwaho

## Slide 74: Tidal power generation
Classification
Single reservoir – single flow system
Generate only in ebb
Single reservoir – double flow system
Henerate in both flow and ebb
Double reservoir – connection system
    High level reservoir, low level reservoir
Generate continuously, low efficiency
Double reservoir – isolation system
    Two single reservoir (single flow) system

## Slide 75: Tidal power generation
Turbines in tidal power station : Bulb turbine
Plant in Rance(France) used this model
Making access for maintenance difficult
 water must be prevented from flowing past the turbine for maintenance
Bulb turbine

## Slide 76: Tidal power generation
Turbines in tidal power station : Rim turbine
Plant in Annapolis(Canada) used this model
Reduce maintenance problems as the generator is mounted in the barrage
Difficult to regulate the performance of these turbines and it is unsuitable for use in pumping
Rim turbine

## Slide 77: Tidal power generation
Turbines in tidal power station : Tubular turbine
The blades are connected to a long shaft and orientated at an angle so that the generator is sitting on top of the barrage.
Tubular turbine

## Slide 78: Tidal power generation
Tidal turbines
Use tidal power directly like wind turbine
Reduced environment problem in comparison with conventional system
Relatively small capacity
Present no difficulty to migrating fish
Tidal turbines

## Slide 79: Tidal power generation
Tidal fences
Effective barrages which completely block a channel
All the electrical equipment (generators and transformers) can be kept high above the water (Good for maintenance)
Reduced environmental problem
Tidal fence is established The islands of Dalpiri in Philippines (1100kW)
Tidal fences

## Slide 80: Tidal power generation
Tidal power plant in Rance
Examples

## Slide 81: Tidal power generation
Water turbine
Tidal power generation Turbine
Examples