Homework 1

Due Date: Oct. 8, 2007

- Using only the following axioms of Boolean algebra:
1. the set of elements contains at least two elements 
2. closure 
3. identity 
4. complementarity
5. commutativity 
6. distributivity,
prove

  - A + A’B = A + B
A+A’B=(A+A’)(A+B)  	-- distributivity
     =1(A+B) 		-- complementarity
     =(A+B)1 		-- commutativity
     =A+B 		-- identity

  - 0 is unique
Assume there are two 0s, 01 and 02.
Then a1+01=a1 and a2+02=a2 by identity.
Let a1=02 and a2=01.
Then 02+01=02 and 01+02=01.
By commutativity, 02+01=01+02.
Therefore 02=01, which implies that 0 is unique.

- Use the Karnaugh map method to find the minimized product of sums expressions for the following Boolean functions:

  - f(A,B,C)=(A xnor B) xnor C

| AB C | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 0 | 1 | 0 | 1 |
| 1 | 1 | 0 | 1 | 0 |

f(A,B,C)=(A+B+C)(A'+B'+C)(A+B'+C')(A'+B+C')

  - f(A,B,C,D)=m(3,4,5,6)+d(10,11,12,13,14,15)]

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 | 1 | x | 0 |
| 01 | 0 | 1 | x | 0 |
| 11 | 1 | 0 | x | x |
| 10 | 0 | 1 | x | x |

f(A,B,C,D)=(B+C)(B+D)(B'+C'+D’)

- Given a function f(A,B,C,D)= [m(1,5,7,8,9,13,15)+d(4,14)], find the minimum sum of products form using the Quine-McCluskey method. Show your process of deriving the prime implicants. Include the implication chart from which your minimum sum of products form is derived.

| m1 | 0001( | -001( | --01 |
| --- | --- | --- | --- |
| d4 | 0100( | 0-01( | -1-1 |
| m8 | 1000( | 010- |  |
| m9 | 1001( | 100- |  |
| m5 | 0101( | 1-01( |  |
| m7 | 0111( | 01-1 |  |
| m13 | 1101( | -101( |  |
| d14 | 1110( | -111( |  |
| m15 | 1111( | 111- |  |

|  | m1 0001 | m5 0101 | m7 0111 | m8 1000 | m9 1001 | m13 1101 | m15 1111 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 010- |  | x |  |  |  |  |  |
| 100- |  |  |  | x | x |  |  |
| 01-1 |  | x | x |  |  |  |  |
| 111- |  |  |  |  |  |  | x |
| --01 | x | x |  |  | x | x |  |
| -1-1 |  | x | x |  |  | x | x |

--01 and 100- are essential.

Remove them and remove the covered columns (m1, m5, m8, m9, m13).

|  | m7 0111 | m15 1111 |
| --- | --- | --- |
| 010- |  |  |
| 01-1 | x |  |
| 111- |  | x |
| -1-1 | x | x |

-1-1 covers both m7 and m15.

Therefore, f(A,B,C,D)=C'D+AB'C'+BD.

- Draw schematic diagrams for the following expressions, using NAND gates only (inverters are not allowed; complemented inputs are available).

  - (AB+CD)E +F

(AB+CD)E +F	=((AB+CD)E +F)''

=(((AB+CD)E)'F')'

=(((AB+CD)''E)'F')'

=((((AB)'(CD)')'E)'F')'
	Schematic is omitted.

  - AB’(B’+C)D’+A’

AB'(B'+C)D'+A'=(AB'(B'+C)D'+A')''

=((AB'(B'+C)D')'A)'

=((AB'(B'+C)''D')'A)'

=((AB'(BC')'D')'A)'

Schematic is omitted.

- Implement the following functions using AND-OR-Invert gates. Assume no limitations on inputs or the number of stacks. You may assume that literals and their complements are available

  - f(A,B,C)=(A xnor B) xnor C

f'(A,B,C)=((A xnor B) xnor C)'

| AB C | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 1 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 |

f(A,B,C)=(A'B'C'+ ABC'+ A'BC +AB'C)'

Schematic is omitted.

  - f(A,B,C,D) =m(3,4,5,6)+d(10,11,12,13,14,15)]

f’(A,B,C,D) =(m(3,4,5,6)+d(10,11,12,13,14,15)])’

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | x | 1 |
| 01 | 1 | 0 | x | 1 |
| 11 | 0 | 1 | x | x |
| 10 | 1 | 0 | x | x |

f(A,B,C,D)=(B’C’+B’D’+BCD)’
	Schematic is omitted.