MVG HW #2  Due 5/21 (Wed)

Mosaicing and Camera Calibration

(Mosaicing) For a given set of 5 images of a rotating camera,

- Determine the homographies .

- Determine the relative rotation angle between consecutive cameras, .

- Mosaic these images by warping other images to the image 3. (Backward warping is recommended for better visualization)

(Camera Calibration) For given two images of an uncalibrated camera,

- Determine three corresponding orthogonal vanishing points in both images.

- Determine the infinity homography between two images.

- Determine the calibration matrix K with zero skew and square pixel using the Cholesky decomposition of.

- What you have to submit:

- Report (doc) that includes the summary of your approach, detailed settings, the results, analysis and discussion.

- Code

- E-mail to me (kyoungmu@snu.ac.kr) above materials in a single zip file with the name “MVG_HW#2_your name.zip”.