동역학 446.204A 003

과제물 #5 모범 답안

14.74

(almost no air flow velocity just above the rotor rotating plane)

Therefore,

The maximum load that the helicopter can lift is obtained by subtracting the helicopter weight from the total thrust calculated above.

4.39

15.31 Angular velocity of disk B after 6s,

Angular acceleration of disk A,

(where the sign of rotation is selected as positive when it is counterclockwise)

Angular acceleration of disk B,

15.57 (a) Absolute velocity at B due to rotation of crank AB

The general plane motion can be considered as sum of a translation and a rotation as follows.

=			+

Since there are no horizontal components in both vB and vD/B, vD = 0.

Therefore, the velocity of the piston is equal to zero.

(b) Absolute velocity at B due to rotation of crank AB

In this case, the vector diagram is drawn as follows.

=			+

Since there are only vertical components in both vB and vD, vD/B = 0.

Therefore, the angular velocity of the connecting rod (BD = 0.

15.69 Angular velocity of the wheel

(a)

Absolute velocity at A can be obtained from the separation of general plane motion into a translation and a rotation considering the rotation of the wheel as follows.

=			  +

Absolute velocity at B can be obtained from the same procedure considering the general plane motion of the rod AB as follows.

=			+

Since there are only horizontal components in both vA and vB, vA/B = 0.

Therefore, the angular velocity of the rod (AB = 0.

(b)

Absolute velocity at A can be obtained from the same procedure as above considering the rotation of the wheel as follows.

=			  +

Absolute velocity at B can be obtained from the same procedure as above considering the general plane motion of the rod AB as follows.

=			+

Since there is only horizontal component in both vB, the vector diagram is drawn as above. From the trigonometry,

15.89 In order to locate the instantaneous center of rotation, lines perpendicular to the velocity vector at each end of the rod AB are drawn as follows.

From trigonometry,

The velocities at A and B are as follows.

15.116 At point A, the drum assembly makes contact with the stationary surface. Therefore, absolute velocity of the drum assembly at A is zero.

Considering the general plane motion as sum of a translation and a rotation,

=			  +

(1)

At B, absolute velocity of the drum assembly should be the same as that of the cord. Considering the general plane motion as sum of a translation and a rotation,

(2)

(1)	(2):

At A, tangential component of the absolute acceleration of the drum assembly is zero since the assembly has a contact with the stationary surface.

Considering the general plane motion as sum of a translation and a rotation,

Horizontal component (i.e., tangential component) of aA should be zero.

(3)

At B, tangential component of the absolute acceleration of the drum assembly is the same as that of the cord.

(4)

(3)	(4):

Using the results obtained above, the accelerations of the points A, B, and C can be computed as follows.

15.156 Use the formula of the absolute acceleration based on the rotating frame of reference as follows.

P1:

P2:

P3:

(P3 is rotating in a circular slot)

P4:

15.172 Use the formula of the absolute acceleration based on the rotating frame of reference as follows.

(a)

(b)

(c)

7.7

7.9

# Text boxes

a

b

IC