2009 BME intro. Assignment 4

2009-04-07

Your name:             ID#:             Department:

Again submit Handwritten Reports:

- Design an amplifier for ECG measurement. A total of six OP Amp will be used. The first three op-amps comprise the instrumentation amplifier necessary to obtain the biosignal and to reject noise.  The fourth and fifth op-amps are designed to be high- and low-pass filters with cut-off frequencies of 0.5 Hz and 100 Hz, respectively.  The last op-amp is a comparator designed to trigger an LED during the QRS-wave portion (This portion has the highest amplitude of about 0.5 mV at the input) of the biosignal.  Between the output of the fifth op-amp and in the input of the sixth op-amp is the output signal of the ECG.  Design for a gain of about 50 and 200 for the first and second stage amplifiers, for a total gain around 104. (Minimum values for resistors for each stage: starting from the first stage, 1K, 1K, 330K, 1.5K, 100 Ohms, respectively). The comparator should detect peaks with amplitudes greater than 0.5 V to trigger an LED.

- Determine the phase margin for the following circuits.  Assume the response of the     OP amp given in the class (power point page 22).

Values of R1 and R2 in ohms (Ro=100 ohms for all)

(a) 1 M, 1M

(b) 1K, 1M

(c) 1M, 1M plus 0.1 uF load

Figures  for problem 1 and problem 2

problem 1.

problem 2.

# Text boxes

Stage 5:

Comparator+

LED

Rmin=100

Stage 4:

Low Pass filter

Gain=1

Rmin=1.5K

Stage 3:

High pass filter

Gain=1

Rmin=330K

Stage 2:

Differential Amp stage

Gain = 200

Rmin=1K

Stage 1 :

Input Stage

Gain=50 Rmin=1K

3)

0.1uF

100

1M

+

-

+

-

Vin

1M

Vout

2)

100

1K

+

-

+

-

Vin

1M

Vout

1)

R0=100

R1=1M

+

-

+

-

Vin

R2=1M

Vout