Water Wave Mechanics ('08 Spring)

Mid-Term Exam

1 (20) The equations for an average viscous flow through a porous medium are defined by

where  is the hydrostatic pressure and  is a constant. Demonstrate that such a flow is irrotational. On the other hand, the equations for an average fully turbulent flow through rocks are

Demonstrate that such a flow is in general rotational.

2 (30) Often the seabed is covered with ripples. The total still-water depth, , can be described as , where is a slowly varying depth and  represents rapid undulations of the depth about  as shown below (Kirby, 1986, JFM, Vol. 162). We assume

(a) Find the exact bottom boundary condition.

(b) Find the bottom boundary condition to  by expanding the bottom boundary condition about .

3 (25) A small amplitude wave of period  = 6.28 s, has traveled over a gently sloping bottom from deep water to a depth of 9 m, where it is observed to have a wave height  = 0.9 m.

- What is the wave length and the phase velocity of the wave in 9 m of water?

(b) What is the deep water wave height, ? Assume the waves to be of normal incidence.

4 (25) Waves generated by a storm range in periods () from 5 to 20 seconds. Assuming deep-water conditions for the entire travel distance, apply the linear wave theory to construct a rough graph of travel time versus  for a beach 1,000 km from the storm area. How much later do the 5-s waves arrive at the beach than the 20-s waves?