Water Wave Mechanics (’08 Spring)

Final Exam (2 hours)

1. (30) For the long waves past an abrupt channel transition (from channel width  and depth  to width and depth ), we obtained the reflection and transmission coefficients as

respectively. Show that these solutions satisfy the conservation of energy.

2. (40) A cylinder with radius  and draft  is heaving (moving vertically) with a velocity  in shallow water of depth .

(a) Express the stroke of the cylinder in terms of  and .

(b) Calculate the wave height near the cylinder generated by this motion.

(c) Calculate the time-averaged kinetic energy of the cylinder. Assume that the volume of the cylinder is constant as  regardless the phase.

(d) The cylinder motion is being damped due to wave generation. If the velocity is reduced to  after one wave period, calculate  using the energy conservation. Note that the difference of time-mean kinetic energy of the cylinder is the same as the energy flux away from the cylinder.

3. (30) Inside surf zone, the Rayleigh distribution is given by

(for example, see Goda (1975), Coastal Engineering in Japan, Vol. 18).  in offshore area as in Eq. (7.13) of the textbook.

(a) Derive the expression for the wave height that is exceeded by  of the waves by the similar manner as that used to derive Eq. (7.17) in the textbook.

(b) Derive the expression for  similar to Eq. (7.20) in the textbook.

Hint: Obtain the Rayleigh probability density function, , using the above Rayleigh distribution, and use  when you change the integral w.r.t.  to the integral w.r.t.  as in Eq. (7.20) in the textbook.

(c) Compare  in offshore area () and inside surf zone (), and provide a possible explanation for the difference.