’08 Final Exam

Engineering Properties in Soils

- Explain the end fiction effect in triaxial test and the ways to reduce it. (10)

- Give the shear tests which can consider 3-dimensional conditions and explain briefly how to perform these tests. (10)

- Explain the effects of particle size and shape on the plasticity index. (10)

- Describe all the calibrations and corrections for hydrometer test on particle size analysis required to obtain reliable results. (10)

- Explain why the consolidation rate decreases as consolidation proceeds based on Darcy’s law. (10)

- Draw the typical results of standard consolidation test and give the soil parameters to obtain the tests. (15)

- Explain the major reasons for the variation of the measured coefficient of permeability, k (the reason for the difference between in-situ k values and k values obtained from the lab test.)  (10)

- Explain the mechanical characteristics of soils compacted on wet side of OMC. (10)

- Give the two in-situ tests to be capable to obtain the reliable mechanical properties (both shearing and consolidation properties) on soft clays or loose sands. (10)

- What is the most suitable boring method for shallow soil layer overlying weathered, soft and hard rock layers. (10)

- What are the measured values in CPT test?  How do we determine undrained strength with CPT results? (10)

- What are the advantages of piston sampler over general thin wall open-drive sampler (shelby tube sampler)? (10)

- In the experiment set up as shown below, flow is taking place under a constant head through the soils A and B of different hydraulic properties.

- Determine the hydraulic head and piezometric head at point X. (5)

- If 35% of the excess hydrostatic pressure is lost in flowing through soil A, what are the hydraulic and piezometric heads at point Y? (5)

- If the permeability of soil A is 0.40 mm/sec, what quantity of water is flowing through unit plan area of soil (=1 m2) per second? (5)

- What is the coefficient of permeability of soil B? (5)

- To determine shearing behavior of normally consolidated clayey soils obtained from 10 m depth as shown below, triaxial tests were performed based on recompression approach and test results are presented in the figures.  Then, answer the following questions.

- Explain test procedures and test conditions with stress conditions (K0=0.6). (10)

- What are the undrained strength, the normalized undrained strength, and pore pressure parameter at failure Af. (10)

- Draw the points of both total stress and effective stress before shearing and at peak, together with failure envelope in the p(p’)-q diagram.  Indicate all the stresses and slope of envelope. (10)