SIGNAL and SYSTEMS		 May 20, 2009

(Instructor : In-Joong Ha, Professor)

EXAM II

[Problem 1] (20points) Consider the system S shown in Fig. 1, with the following input

.				    (1.1)

The impulse response of channel is

(1.2)

and the impulse response of the ideal low pass filter is

.					 (1.3)

- Sketch Fourier transform of the output .

- Find impulse response  of the system S and its Fourier transform.

Fig. 1

[Problem 2] (20points) Suppose that a discrete-time system H can be described by the following discrete-time state vector difference equation.

(2.1)

where , while are constant matrices with appropriate dimensions.

- Assume that the Fourier transforms of the input and the impulse response of the system H exist. Then, show that

(2.2)

- Suppose that the constant matrices  are given by

(2.3)

Then, determine specifically the impulse and frequency responses of the system H. Further, find the difference equation in terms of , which has the same frequency response of the system H.

[Problem 3] (20points) A particular discrete-time system has input  and output . The Fourier transforms of these signals are related by the equation

(3.1)

- Is the system linear? Cleary justify your answer.

- Is the system time invariant? Cleary justify your answer.

- What is  if ?

[Problem 4] (20points) Let  denote the unit sample response of a desired ideal system with frequency response , and let  denote the unit sample response for an FIR system of length  and with frequency response . In this problem, we show that a rectangular window of length  samples applied to  will produce a unit sample response  such that the mean square error

(4.1)

is minimized.

- The error function can be expressed as the power series

(4.2)

Find the coefficients  in terms of  and .

- Using Parseval’s relation, express the mean square error  in terms of the coefficients .

- Show that for a unit sample response  of length samples,  is minimized when

(4.3)

That is, simple truncation gives the best mean square approximation to a desired frequency response for a fixed value of .

[Problem 5] (20points) Consider a band pass filter whose frequency response is specified as

.		              (5.1)

- Find the impulse response of equation (5.1).

- An ideal band-pass filter can be approximated by cascading a first-order low-pass and a first-order high-pass filter. Sketch the Bode plot for system S as shown in Fig. 2.

Fig. 2

-  E N D -