Coastal Structures (’14 Fall)

Final Exam

(Open book, 1 hr 50 min)

1. (30) A two-dimensional hydraulic model test with the length scale of  is made of a vertical revetment constructed on a beach with the bottom slope of 1/30. The equivalent deepwater wave height and significant wave period are 4.4 m and 12 s, respectively. The water depth at the location of the structure is  m (i.e. 0.3 m in the model). Due to the limited height and length of the wave flume, the plane slope of 1/30 is extended only to the depth of 0.6 m so that the water depth is constant as 0.6 m from the seaward end of the slope to the wavemaker.

(a) Calculate the significant wave height and period of the waves that should be generated by the wavemaker.

(b) The structure is constructed to protect a densely populated coastal area for which the allowable overtopping rate is 0.01 m3/s/m. Calculate the allowable overtopping rate per unit length in the model.

(c) Also calculate the allowable total overtopping amount per unit length during the storm duration of 2 hours in prototype and its correspondence in the model.

2. (40) Jackson (1968) proposed an empirical equation for run-up of regular waves on a Tetrapod-covered slope as

where  is the incident wave height, and  is the Iribarren number;  is the slope angle and  is the deepwater wavelength. Waves of  m and s are normally incident to a seawall having 1:1.5 slope and crest elevation of 1.5 m. Assume that the Jackson’s equation can be used for calculation of individual wave run-up of irregular waves. You may need the table for normal distribution.

(a) Calculate the smallest wave period for 2 m high waves to overtop the seawall.

(b) Calculate the probability of waves of 2 m height to overtop the seawall.

3. In the reliability-based design called the LRFD (Load and Resistance Factor Design), the L-year maximum wave height is often used, which is the expected value of the largest wave height during the L years of the design life time of the structure. The 100-year wave height of the Kodiak data (see Tables 13.3 and 13.4 in textbook) has been estimated as  m in Section 13.2.2(E) by the Weibull distribution with ,  and . For the Kodiak data,  years, , , , and the sample standard deviation  m.

(a) For 100-year design life time of a structure, calculate the 100-year maximum wave height  and its standard deviation .

(b) Calculate the coefficient of variation .

(c) Calculate the 90% confidence interval of .