P1

Fig.1 shows series-shunt amplifier with a feed back factor . The amplifier is designed so that  for , with small deviations in  from 0V dc being minimized by negative-feedback action. The technology has  , and ,

- With the feedback loop opend and the gate terminals of Q1 and Q2 grounded, find the dc current and overdrive voltage at which Q1 toQ5 is operating. Ignore the mismatch  between Q1 and Q2  arising from their different drain voltage. Also find dc voltage at the output

- Find  and  of each of the five transistors

- Find the values of A and Ro. Assuming that the bias current sources are ideal

- Find the gain-with-feedback, , and the output resistance Rout

- How would you modify the circuit to realize a closed-lood voltage gain of 6V/V?

What is value of output resistance obtained?

Fig. 1

P2

| NPN | 200 | 125V | 10^(-14) |
| --- | --- | --- | --- |
| PNP | 50 | 50V | 10^(-14) |

Condition : neglect capacitances inside transistor

1)   find the DC bias point and draw small signal equivalent circuit with corresponding small signal parameter (

2)   find open-loop gain (A)

3)   calculate   when Rf = 50 kOhm , Cf =

4)   Draw frequency response of the amplifier (Bode plot, gain, phase)

When Rf = 0 Ohm , Cf = 30 pF

- Determine the value of Rf that results in the phase margin of

P3

Condition : Transistor parameter is same as P2

All Transistor is same

- Find the value of  that gives the base voltage bias  of 1.0 V

- Draw small-signal equivalent circuit of output stage

(hint : replace the bias circuit by its equivalent resistance)

- This circuit (with this bias) cannot generate a symmetric voltage swing at NPN(Q14), PNP(Q20) transistors. Explain why.

- Determine the range of , which allow symmetric operation

(hint : For getting a symmetric swing, input resistance of transistor must be

similar)

P4

Consider the actively loaded CE amp with emitter degeneration.

Let  I = 100 mA,  =100V ,  , Re = 75 Ohm , Rsig = 5 kOhm

- Which type of feedback is this circuit ?

- Find

- Re is now replaced with a series of  resistor and capacitor as follow.

Find the value of ‘Ce’ that makes this amplifier unstable .

(Hint :if gain >1 , Rout <0, the circuit is unstable.)