# Chapter 1  Introduction

# 1. Current Problems or Issues in Nuclear Thermal-Hydraulics

☛ TMI-2 accident highlighted code deficiencies

; More physical phenomena were involved in the treatment. (e.g., core

heatup, pressurizer discharge, secondary side voiding and filling, etc)

☛ Advanced and new nuclear reactors are under development in many countries.

# (1) Code development

- Improve and maintain reactor safety codes

- Lack of data for development of models/correlation and code validation

▶ GEN-IV reactors

- Uncertainty evaluation and methodology development for existing and

new reactors

- Development of multidimensional and multiphase system code

▶ TRAC, MARS, or MARS/MASTER(coupling of T/H and neutronics)

▶ GAMMA, MARS-GCR

- Development of system codes for new reactors

- Application of CFD codes and combination with system codes

▶ quality assurance for CFD codes and identification of the weakness of

CFD techniques

# (2) Experiment

- Small scale experiments to improve two-phase flow formulation and

constitutive relations

- Maintain experimental facilities and conduct experiments for code

validation and better understanding of thermal-hydraulic phenomena

# Fig. 1.1 Overview of Process

# (3) Goal of NRC TH Code Development

● A state-of-art TH code capable of performing accident and transient

analysis for operating LWR as well as advanced passive reactors

● Must have capabilities suited to address safety-significant issues

that pose challenge to current codes, which require;

- coupled RCS TH and containment feedback

- coupled RCS TH and neutron kinetics

● Evolutionary improvement in current capabilities

☞ ease of use

☞ accuracy - improved two-phase flow and physical models

☞ speed

☞ robustness

# 2. Current Research Activities in the Field of Nuclear Thermal-Hydraulics

☛  Researches on existing NPPs

• focused on safety

- to resolve safety issues

- to ensure NPP safety due to power uprates and continued operation for operating NPPs

- to ensure NPP safety due to new safety features for new NPP designs

☛  Researches on next generation NPPs

• development researches to makeup technology gap

• safety researches for NPP safety

# (1) System code application and development

- Computer simulation is the only way of knowing how the plant will respond to normal and accidental conditions.

● Modeling Philosophy

☞ 1970's Appraoch

- use more complete set of field equations

(Ex: replace HEM with two-fluid model)

- model physical processes from "first principles"

(Ex : bubbly flow interphase drag computed as drag on sphere with diameter from Weber # criteria.)

- use generic volumes & junctions

(i.e. a volume in a pipe is treated the same as a volume in the core or a volume in the pressurizer, etc)

☞ Proposed Approach

- Constitutive models should be physically based.

․ empiricism is used two-phase flow in complex geometries

․ component specific closure relation.(eq. interfacial shear in a tube does not represent that in rod bundle nor in the downcomer)

- Component Models:

․ accumulators as an example (See Model and Correlation)

- Explore inprovements to two-phase model:

․ addition of droplet field(annular mist & reflood)

․ dynamic flow regime model(interfacial area transport)

● Model and Correlation

☞ "Zero-D" Component Models

- Code accuracy, efficiency and simplicity can be improved by using single volumes with special analytical/empirical models to better represent the physics (eq. accumulators)

● Improve Constitutive Relations:

- Accuracy : systematic program by detailed experiment, better use of current data base

: component specific relations & development within two-fluid framework.

(Ex) Pipe vs. Rod Bundle interfacial friction

coefficient

- Consistency : the treatment of flow regimes and constitutive models should be consistent (eg, interfacial friction & heat transfer should use same flow regime)

- Numerical Characteristics : remove unphysical discontinuities, base correlations on integral variables when possible and build-in physical time scales.

● Model Selection Process:

- Use PIRT (Phenomena ldentification & Ranking Table) to guide model selection process (focus effort).

- Review of current codes (NRC & others) and literature

- Assemble suitable data base

󰋯 may require separate effect testing

- Perform quantitative model comparisons

- Select best overall model (or develop new model)

󰋯 peer review procces

󰋯 data base & computational results -> model documentation

( Activities for system code development

- Korean Activities

▶ For the existing reactors

o MARS code consolidation (KINS)

- DVI model for APR1400

- Validation of 3-D capabilities

- Code coupling

o Development of numerical technique with a high

precision (KAERI)

- Multi-dimensional models for two-phase flow and interfacial transport phenomenon                  [KINS-REM]

- Numerical scheme

- Multi-dimensional component modules (RCS, SG, etc)

o Development of domestic design code system (KHNP)

- Secure his own property

▶ For new reactors

o A current focus is to modify LWR

safety codes.

o Extension of MARS code to new

reactors (KAERI)

- MARS-SMART

- MARS-GCR

- MARS-LBE

o Challenges

- New fuels, Different coolants, Higher temperature operating conditions,

- Events relevant to high-temperature gas-cooled reactors differ from those in LWR’s

- New severe accident models are needed to describe phenomena peculiar to the future reactors

2) International activities

- Very similar to Korean activities

- Code application to evaluate safety issues

- Code application to check the existing code applicability for new reactors

▶ For the existing reactors

o TRACE code development (USNRC)

- Spacer grid models

- Droplet field & entrainment modeling

- Interfacial drag models

o NEPTUNE project (France IRSN)

- Multi-scale and multi-disciplinary calculations (CATHARE + CFD)

- To prepare the new generation of industrial two-phase flow codes

- To structure and coordinate the R&D works around two-phase flow

# ▶ Activities in the States for New Reactors

- Gas-cooled reactor codes ; GRSAC

- LWR codes ; ATHENA + FLUENT + CONTAIN, MAAP4, MANTRA,

MELCOR, RELAP5-3D, etc

  - Experiment

# (2) CFD Code Application

- CFD codes are mainly capable of

obtaining at a lower cost, valuable

information on some physical

phenomena.

- Problems

  - How to validate CFD code and make results reliable?

  - How to apply multi-component and multi-phase problems?

- Single-phase problems for the existing reactors

  - Boron dilution

  - Mixing of cold and hot water in Steam Line Break event

  - Hot-leg temperature heterogeneity

  - PTS (pressurised thermal shock)

  - Counter-current flow of hot steam in hot leg for severe accident investigations of a possible “Induced Break”

  - Thermal fatigue (e.g. T-junction)

  - Hydrogen distribution and combustion in containment

- Two-phase problems where CFD is recommended

☛ Two-pahse CFD tools are far less mature

than single phase tools.

  - Identification of the relevant basic phenomena which need to be modeled for a given application

  - Assessment of the model including verification, validation and demonstration tests

  - Definition of new R&D work for a more detailed validation, for a better numerical efficiency, and a better accuracy and reliability of predictions

(3) Experimental researches

  - To investigate real phenomena and/or prove system performance

  - To provide technical basis for the development of models and correlations

▶ Status of Korean experimental technology and infra

  - Separate Effect Tests

- world-wide top level of high-temperature/high-pressure test and

measurement technology

- conducting researches with several test facilities for development of critical models in thermal-hydraulics under the long-term nuclear R&D program

- produce in earnest the detail data to assess the code models

- partly develop the local models to describe the characteristics of

Korean reactors

- But, still dissatisfied development of localized model by our own

experiment

  - Integral Effect Tests

- Construction of ATLAS secured the IET system to support the regulation of Korean nuclear design and construction.

- simulate most accident scenarios for APR1400 and OPR1000 which are hard with foreign data

⇒ secure the compatibility of design and regulatory code

- But, need new IET facilities for new reactors such as SMART which has different design characteristics.

(4) Thermal Hydraulic Issues in the development of SMR (Small-Medium

Reactor)

● Natural circulation for core cooling

- 3D phenomena of local as well as global scale

- optimizing component arrangement

- under low pressure of normal operation

- decay heat removal under accident conditions

✓ interaction between heat source and sink

✓ turbulence mixing

✓ buoyancy effect on turbulent flow

✓ natural circulation CHF mechanism

✓ thermal stratification

✓ non-condensible gas behavior and its influence on condensation

● Thermal hydraulic instability in helical coiled team generator