Water Treatment

1. 	Introduction

- See Fig. 9-1 (p.325): Relationship between the drinking water treatment and the waterborne diseases

-	See Fig. 9-2 (p.329): Flow diagram of conventional surface water treatment plant

1.1 History

| 연대 | 취수원 | 급수 | 정수 | 국내 |
| --- | --- | --- | --- | --- |
|  | 지표수 우물 | 석재수로 목관 연관 | 햇빛 목탄 가열 |  |
| 1582 1800 1895 |  | Pump 주철관 | 완속여과지 | - 1894. 부산 보수천 집수설비, 자연여과, 배수지 설치 - 1908. 서울 뚝도 정수장 준공, 125,000명, 100 L/인,일 |
| 20 세기 |  |  | 급속여과지 소독 | - 2001. 상수도 보급률 87.8%, 361 L/인,일 (공업용수 제외 수치, 인천광역시 428L, 광주광역시 297L). |
| 현재 |  |  | 색깔 및 냄새 독성물질 심해수 이용 고심도 송수 | - 취수원 수질 악화 - 물 부족 - 누수 - 바이러스, cryptosporidium, giadia |

- Cryptosporidium: 400,000 illinesses, 50-100 deaths, in Milwaukee, WI., 1993

- Cryptosporidium (3-7 (m), Giadia (8-18 (m)

- Portable water (safe) and Palatable water (pleasing)

1.2	Water Quality Standards

미생물에 대한 기준

-	Indicator-microorganism (지표미생물) :

-	물 속의 주요한 수인성 질환 병원체 : 세균(e.g., 살모넬라), 바이러스, 원충(e.g., cryptosporidium)

건강상 유해영향을 주는 무기물질

- 납, 수은, 비소, 카드뮴, 6가 크롬, 세레늄 등의 중금속 : 축적성 독성물질

- 암모니아 (유기질소에서 기인), 질산성 질소, 유독성 시안, 불소 등

건강상 유해영향을 주는 유기물질

- Solvents : Phenol, Dichloromethane, benzene, toluene, etc.

-	농약류 : 디아지논, 말라티온, 파라티온 등

-	DBPs (                           ) : Trihalomethane

심미적인 영향을 주는 물질

-	직접적인 건강상의 유해물질은 아니지만, 먹는 물로 사용하는 데에 부적절한 영향물질

-

2. Unit Processes

2.1	Coagulation

- to turn the small particles of color, turbidity, and bacteria into larger flocs, either as precipitates or suspended particles

- Colloidal particles are (1) too small to settle in a reasonable time period, (2) too small to be trapped in the pores of a filter, and (3) stable due to their negative charge.

Mechanisms

- Adsorption and destabilization: extremely fast within 1 second

- Sweep coagulation: 1 to 7 seconds

- Using the Jar test, which mechanism is predominant can be identified.

Key properties of a coagulant

## Aluminum

-	liquid alum (or dry) : Al2(SO4)314H2O

-

-	When sufficient alkalinity is not present, the pH may be greatly reduced.

- The aluminum ion does not really exits as Al3+ and the final product is more complex than Al(OH)3, for example, Al8(OH)2028H2O]4+.

## Iron

-	Dry and liquid forms : Fe2(SO4)3 xH2O or FeCl3 xH2O

-

-	Ferric salts generally have a wider pH range for effective coagulation than aluminum.

Coagulant aids

- pH adjusters:

-	Polymers: long-chained carbon compounds of high molecular weight that have many active sites and produce a larger flocs (i.e., interparticle bridging).

2.2	Mixing and Flocculation

Rapid Mixing

- The coagulation reaction is completed very fast. Thus, the mixing should be as instantaneous and complete as possible.

- Apparatus: see Fig. 9-5 (p. 334)

Flocculation

-	to bring particles into contact so that they will collide, stick together, and grow to a bigger size.

- Apparatus: see Fig. 9-6 (p.335)

2.3	Sedimentation

## Overview

- Sedimentation basin or Clarifier

- Rectangular or Circular

- Radial flow or Upflow

- Inlet, Settling, Outlet, and Sludge storage (See Fig. 9-14, 15, p.347)

##### Inlet : 	to evenly distribute the flow and suspended particles

to reduce the water velocity to the settling zone design velocity

consists of a series of inlet pipes and baffles

Sludge storage :	the method of cleaning, the frequency of cleaning, and the quantity of sludge

with bottom slope or sludge hopper, bottom scraper

Settling :

where	v = water velocity, m/s;

Q = water flow, m3/sec; and

As = cross-sectional area, m2.

# Outlet :	Weirs (See Fig. 9-15, p.349)to prevent “scouring”, i.e., washing out of the floc

Weir overflow rate = [m3/day,m]

## Sedimentation Concept

-	Settling velocity and Overflow rate

-	For the upflow clarifier, the settling velocity (vs) > liquid-rise velocity (vo)

As long as vs is greater than vo, the particle will settle downward regardless of the depth.

- For the horizontal clarifier, the removal efficiency dependent on the overflow rate, vo ( is “overflow rate”),

- In order to remove particles, vs > h/t0 (see Fig. 3.33, p. 217) and

(overflow rate)

The removal efficiency is independent of depth.

(see Fig. 3.34, p.218)

Determination of vs

where	FG = gravitational force;

FB = buoyancy force;

FD = drag force;

(s = density of a particle;

( = density of fluid;

g = acceleration due to gravity;

Vp = volume of the particle;

CD = drag coefficient;

Ap = cross sectional area of the particle; and

vs = velocity of the particle;

The driving force for acceleration of the particle is,

When the drag force is equal to the driving force, the particle velocity reaches a constant value called the terminal settling velocity (vs).

For a spherical particles with a diameter = d

#### CD vs. Reynolds number (by Thomas Camp, see Fig. 3.36, p.223)

Stokes’ law (Terminal settling velocity for a sphere under laminar flow condition)

## Sludge Blanket

- Mixing, flocculation, and clarification can be conducted in a single reactor. “Sludge blanket”– an upflow solid-contact basin.

2.4	Filtration

-	to separate suspended (or colloidal impurities) from water

- media : sand, coal (anthracite), dual media (coal-lighter than sand + sand), or mixed media (coal, sand, and granite)

-	Loading rate

where	va = loading rate (or face velocity), m3/day,m2;

Q = flow rate onto filter surface, m3/day; and

As = surface area of filter, m2.

Slow sand filter (< 10m3/day,m2) – top layer (e.g., 75mm) is scraped off, cleaned, and replaced.

Rapid sand filter (Fig. 9-17, p.353, > 100m3/day,m2)

High-rate sand filter – upto 800m3/day,m2

2.5	Disinfection

-	Disinfection (소독) vs. Sterilization (멸균)

- Targets: Bacteria, Virus, and Ametic cysts

-	Disinfectants

- destroy pathogens that may be introduced within a practical period of time;

- meet possible fluctuations;

- at reasonable cost and safe, easy to store, transport, handle, and apply;

- determined easily, quickly, and (preferably) automatically;

- persist against possible recontamination

- neither toxic to humans and domestic animals nor unpalatable;

Disinfection Kinetics

Chick’s law (a first order reaction)

Disinfecting Action

-	CT : Product of C and T

-	CT values (mg/L.min) (see Table 3.20, p.244 : 3-log reduction of Giardia is required.)

Chlorine Reactions in Water

-

-	Chlorine gas

(within a very few milliseconds)

(pK = 7.537 at 25oC)

- Sodium hypochlorite

-	Cacium hypochlorite

-	“free available chlorine” : chlorine existing in the form of HOCl and/or OCl-.

-	Optimum pH = 6.5 - 7.5

Chlorine/Ammonia Reactions

-	Chloramines : retain the oxidizing power of the chlorine

(monochloramine)

(dichloramine)

(trichloramine)

- High Cl2:NH3, low temperatures, and low pH, favor dichloramine formation.

- Combined available chlorine(        ): chlorine in chemical combination with ammonia or organic nitrogen compounds

- Combined available chlorine is a less effective disinfectant than free available chlorine(        ). However, it does not produce odor and taste, is reduced more slowly and persists for a long time in the distribution system (Chloramine disinfection).

Breakpoint chlorination, See Fig. 3.44 (p.247)

- 심하게 오염된 원수에 대해, NH3와 취미의 원인이 되는 유기물을 분해하는 데에 필요한 염소요구량 이상의 염소를 주입하는 처리법 (파괴점염소처리법)

- (Cl2:NH3 = 1.5:1.0, breakpoint)

or  3Cl2 + 2NH4+ → N2( + 6HCl + 2H+

then after,  (free available chlorine)

## Other Disinfectants

- Chlorine dioxide(ClO2):

- Ozone(O3):

- Ultraviolet radiation(UV):

3. Additional Treatments

## Adsorption

- GAC(Granular Activated Carbon)

AOP (Advanced Oxidation Processes)

- Hydroxyl radicals (OH(): Highly reactive nonselective oxidants

- Ozone, Hydrogen peroxide (H2O2), and UV

4. Water Treatment Plant Waste Management

The logical sludge management

(1)

(2)

(3)

(4)