## Slide 1: Environmental Thermal Engineering
Lecture # 8
Min Soo Kim
Mechanical & Aerospace Engineering

## Slide 2: Type of refrigerant
Halocarbon CFC, HCFC, HFC, R-12, R-32, R-134a
Hydrocarbon R-50, R-170, R-290, R-600, R-1270
Inorganic compound Ammonia(R-717), water
Carbon dioxide R-744

## Slide 3: Type of refrigerant
CFC (chlorofluorocarbon )
- Compound that consists of carbon, chlorine, fluorine
- R-12, R-113, R-114, R-115
- Most high ODP(Ozone Depletion Potential
- They have an effect on global warming
2. HCFC (hydrochlorofluorocarbon)
Compound of CFC which has at least one hydrogen atom.
R-22, R-123, R-124, R-141b, R-142b
- With substitution of a portion of Cl with H, ODP has reduced
- They have a little effect on global warming
3. HFC (hydrofluorocarbon)
Compound that consists of only carbon, chlorine, hydrogen
R-32, R-125, R-134a, R-143a, R-152a
No influence on Ozone layer

## Slide 4: Notation of refrigerant
Notation (1)
- Expressed on treble figures each digit is related with elements
- Hundreds digit x = the number of carbon atom - 1
- Tens place y = the number of hydrogen atom+ 1
- Unit digit z = the number of fluorine
Methane, Ethane, Propane series
Notation (2)
- Adding 90 on R-xyz, which makes new notation that each digit represent the number of elements
- Hundreds digit x = the number of carbon atom
- Tens place y = the number of hydrogen atom
- Unit digit z = the number of fluorine

## Slide 5: Notation of refrigerant
Notation(3)
In the case that refrigerant is composed of 4 species -carbon, hydrogen, fluorine, and chlorine- the number of chlorine atom is 2x-y-z+5
- In the case that isomer exists, alphabet a or b is added for clarifying according to stability of halogen element
Methane, Ethane, Propane series
H H
| |
F-C-C-F
| |
F F
R-134
H F
| |
H-C-C-F
| |
F F
R-134a
Notation expressed by structure
염소d

## Slide 6: Example
Question) Figure out chemical compound of R-134a
134+90 = 224
Carbon = 2
Hydrogen = 2
Fluorine = 4
Answer)
134
Carbon = 1+1 = 2
Hydrogen = 3 -1 = 2
Fluorine = 4 = 4

## Slide 7: Notation of refrigerant
2. Zeotropic mixture refrigerant
Naming as R-400~
Number and mass composition for component of compound should be specified in the ascending order of the boiling point
3. Azeotropic mixture refrigerant
- Naming as R-500~
4. Organic compound refrigerant
Naming as R-600~
Butane series : R-60O
Oxygen compound : R-61O
Organic compound : R-62O
Nitrogenous compound : R-63O

## Slide 8: Notation of refrigerant
5. Inorganic compound refrigerant
Naming as R-700
Last two digits mean molecular weight
(For example, water is named as R-718)
6. Unsaturated organic refrigerant
Naming as R-1000~
Following notation of halocarbon at the digits under hundreds

## Slide 9: Notation of refrigerant
Refrigerant number of a kind of halocarbons
 | Chemical name | Chemical formula
11 | Trichloromonofluoromethane | 
12 | Dichlorodifluoromethane | 
13 | Chlorotrifluoroethane | 
22 | Monochlorodifloromethane | 
40 | Methyl chloride | 
113 | 1,1,2-Trichlorotrifluoroethane | 
114 | 1,2-Dichlorotetrafluoroethane | 

## Slide 10: Requirements for refrigerant
Thermodynamical properties
- High latent heat
- Low coagulation pressure
- Higher critical temperature than ambient condition
- Higher boiling pressure than ambient condition in low temperature
- Low condensing pressure is recommended
Thermodynamical properties
Physicochemical properties
- High electric resistance of refrigerant vapor
- Good heat transfer property
- Proper solubility to lubricant
- Low hygroscopic
- Chemical stability, no spoilage
- Inactivity, low corrosiveness

## Slide 11: Requirements for refrigerant
Environmental properties
- No flammability and explosiveness
- No toxicity
- Contains are not to be damaged by refrigerant leaking
- Eco-friendly one is recommended
Thermal Engineering Criteria
- Volumetric Capacity
- COP
- Discharge Temperature
- Compression Ratio

## Slide 12: General Characteristic
Flammable
Toxic
Long Atmospheric Life
Available
(HCFC, HFC)
F
H
Cl

## Slide 13: Characteristic of refrigerants
Halocarbon
- Substituting saturated hydro-carbon for halogen series
- Clarified to CFC, HCFC, HFC by a presence of main components – hydrogen, fluorine, chlorine, carbon
- CFC and HCFC is prohibited because of its environmental problem
- R-143a and R-152a in HFC can substitute R-12
- R-32, R-125 and R-143a can be used as azeotropic mixture refrigerant
Hydrocarbon
Refrigerant composed of only hydrogen and carbon
R-50(methane), R-170(ethane), R-290(propane), R-600(butane), R-600a(iso-butane), R-1270(proplene)
Non-toxic, stable, eco-friendly
Large specific volume which makes small quantities of refrigerant injection
Flammability

## Slide 14: Characteristic of refrigerants
Zeotropic mixture refrigerant
Mixture of more than two pure refrigerant
Each refrigerant component has different properties so that composition of mixture changes while boiling and condensing
Temperature rises when boiling, reduces when condensing in constant pressure

## Slide 15: Zeotropic mixture refrigerant
Two-
Phase
region
Superheated
Vapor region
Subcooled liquid
region
Dew line
Bubble line
0
0.4
0.6
0.8
1.0
0.2
65
45
25
5
105
85
Composition(%mol)
Temperature(F)
Phase change curve of R-22/R-114(Zeotropic mixture)

## Slide 16: Zeotropic mixture refrigerant
Adventages
Temperature rises when the refrigerant boils in constant pressure
Temperature reduces when the refrigerant condenses in constant pressure
That is, a temperature gradient occurs in phase changing
Heat exchanger efficiency can be improved by using this charateristic
Temperature,T
S
Refrigerant
Refrigerant
Heat sink
Heat source
Pure refrigerant
Temperature,T
S
Refrigerant
Refrigerant
Heat sink
Heat source
Zeotropic refrigerant
Zeotrpic mixture refrigerant and make temperature of refrigerant and heat source parallel so that mean temperature difference and irreversibility has reduced with efficiency improvement

## Slide 17: Zeotropic mixture refrigerant
Large heat exchange requirement with low temperature difference
2. High cost with counter-flow heat exchanger
Disadvantage
3. The most crucial problem is that when refrigerant leaks, composition changes because component with higher vapor pressure escape first. That is, In the case of re-charging, entire refrigerant should be took back and injected newly.

## Slide 18: Zeotropic mixture refrigerant
Mixture of more than two pure refrigerants
Differently from Zeotropic mixture, temperature is uniform while phase changing in constant pressure
- Behavior of material is similar with pure material
Two-
Phase
region
Superheated
Vapor region
Subcooled liquid
region
Dew line
Bubble line
0
0.4
0.6
0.8
1.0
0.2
40
36
32
28
48
44
Composition(%mol)
Temperature(F)
azeotrope
Phase change curve of R-500(azeotropic mixture)

## Slide 19: Advantages of Mixture refrigerant
Can improve thermodynamical properties
Can improve solubility with oil
Can reduce flammability
Can improve performance

## Slide 20: Attention for environment
After finding out Freon gas and ozone layer destructing effect, attention for environmental pollution by emission has increased. And it is concretized by the climate change conventions.
type | Source
 | Fossil fuel, Forest fire
 | Bacteria, Decomposition of organic matter
 | Combustion, Nitrogenous fertilizer
 | Refrigerant, Spray

## Slide 21: Attention for environment
Carbon dioxide, methane, nitrogen dioxide - criteria for 1990
Alternative refrigerant (HFC, PFC) - criteria for 1995
Developed country plays a leading role for solution for environmental problem
Kyoto Protocol,1997
goal and term is set up : 2008 – 2012
target for reduction
(1) Carbon dioxide, methane, nitrogen dioxide - criteria for 1990
(2) Alternative refrigerant (HFC, PFC, SF6) - criteria for 1995
Net CO2 emissions system and emission rights trade system introduced
Eco-development fund settled – supporting developing countries
reduction goal has legal force
differential application through nations
(1) developing countries is excluded
(2) differentially applied for advanced country, East-European countries

## Slide 22: the Climatic Change Convention
Buenos Aires Plan of Action (1998)
- 170 countries consent with trade permit system, clean production developing system, joint carrying system until the sixth assembly in 2000
Visualization of birth of greenhouse gas market with scale of a billion ton annually
Kyoto Protocol,1997
goal and term are set up : 2008 – 2012
target for reduction
(1) Carbon dioxide, methane, nitrogen dioxide - criteria for 1990
(2) Alternative refrigerant (HFC, PFC, SF6) - criteria for 1995
Net CO2 emissions system and emission rights trade system introduced
Eco-development fund settled – supporting developing countries
reduction goal has legal force
differential application through nations
(1) developing countries is excluded
(2) differentially applied for advanced country, East-European countries

## Slide 23: the Climatic Change Convention
Solution for greenhouse gas prohibition
Strengthening competition of industry
Improvement of efficiency, Alternation of fuel
Forest conservation and reforestation industry
Reduction of greenhouse gas emission
Regulation of emission gas
Current situation of Korea
As Korea has transited to energy conservation industry, Emission of pollutant material has reduced. However, it is still higher than the level of advanced country
Most portion of greenhouse gas is due to energy area which is followed by industrial process area
Greenhouse gas policy of authorities
continuous transition to energy-saving industry is needed
consideration of regulation of greenhouse gas emission and alternative material is needed.

## Slide 24: Type of nature refrigerant
 | Advantage | Disadvantage
 | Good property Working in low pressure | Combustible
 | Good property Used for ship | High pressure High critical temperature and pressure
 | Used in industry (in large scale plant) | Toxic combustible

## Slide 25: Type of nature refrigerant
 | Advantage | Disadvantage
 | Non-toxic Direct usage of refrigerant | System enlargement
 | Non-toxic Applied for high speed Train in Germany | Gas cycle
 | Used in stirring engine | Gas cycle Low efficiency

## Slide 26: Automobile with CO2

## Slide 27: Existing VS Nature

## Slide 28: CO2-A/C- system

## Slide 29: A CO2 Refrigerant system